TECHNICAL FACTSHEET: COLLABORATION BETWEEN GRUPO COSENTINO – SPAIN PAVILION IN THE 2015 MILAN EXPO

Cosentino Group’s collaborates mainly through making available different materials of its leading Dekton® and Silestone® brands. The Dekton® ultra compact surface is an innovative new category of surface created by Consentino with the aim of becoming a leader in the world of international architecture and design, for both indoor and outdoor spaces.

The surface is a sophisticated mixture of raw materials used to make glass, latest-generation porcelain tiles and quartz surfaces. Dekton® is able to recreate any type of material with a high level of quality, it is manufactured in large format planks (320 cm x 144 cm) and minimum thickness (0.8 cm, 1.2 cm and 2 cm), with superior technical properties.

The fact that this material is being applied in the Spain Pavilion is a major achievement and shows the perfect versatility of the product. It is important to note the special characteristics of this unique work:

- Diversity of sizes and thickness:  For example, the pieces applied as flooring in the Pavilion have been placed in up to 6 different measures (14x200cm; 66x134cm; 66x136cm; 70x121cm; 70x136cm; 70x210cm).   And the 3 table top surfaces have measures of 16ml x 0.60m (tapas bar counter); 10ml x 0.80m (auditorium bar counter) and 5.40ml x 0.30m (VIP area)

- External and interior applications:  People visiting the Pavilion will be able to see the material in both internal spaces (exhibition, multi-function room, public space) and also external ones (the square, the vegetable garden).

- Variety of colours, appearances and finishes: The main colours assigned are Zenith (white) and Domoos (black), both of which belong to the Solid collection.

- Different uses and applications: Dekton® is applied as flooring, staircase, worktop, café bar and for external furniture (vegetable garden)

- Personalised inkjet printing:  See the “Tomato genome” application with inkjet printing technique

Dekton® material in the Spain Pavilion

| Modality of the Material | Use or application | Amount | Pavilion Space |
| --- | --- | --- | --- |
| Dekton Zenith 2cm | Flooring | 430m2 | Second Floor |
| Dekton Zenith 2cm | Flooring | 330m2 | Tomato genome floor |
| Dekton Domoos 2cm | Flooring | 100m2 | Auditorium or multi-purpose room |
| Dekton Zenith 2cm | Stairs | 12.40m2 | Stairs with access to restaurant (2nd floor) |
| Dekton Zenith | External applications | 30m2 | Vegetable garden |
| Dekton Zenith 2cm | Table tops | 3 | Auditorium Bar / Tapas Bar / VIP area |

Silestone® Eco Line, also present in the Spain Pavilion

Consentino's contribution is completed with three Armony model wash-hand basins made out of Silestone® for bathrooms. The wash-hand basins with measurements of 90x47 and 120x47 use the Riverbed tone belonging to the Eco Line, the Silestone® ecological alternative. This colours series is manufactured using at least 50% of recycled materials such as glass, crystal or porcelain.

“Tomato genome”: With Dekton®, architects and designers can make their ideas a reality

One of the most attractive and innovative interior design proposals to be found in the Pavilion will be the recreation of the tomato genome in the  Dekton® tables, printed using inkjet technology. The pieces of Dekton® are used to form the flooring of the exhibition and public space on the ground floor.

Within the framework of the “The language of flavour” slogan, the Fermín Vázquez architects studio came up with the idea of recreating the tomato genome - one of the most important recent steps taken in the field of biotechnology and scientific research. The tomato genome was sequenced for the first time in 2012, and this was a major step forward in improving the variety of crops and for the future of agriculture.

This is possible because Dekton® allows a very high level of customisation in design, and is thus the perfect ally for designers and architects all over the world. The customisation has two variations which can be applied separately or together: using milling technology and also through inkjet printing technology. In this specific case, the latter solution has been used for the Spain Pavilion.

Inkjet technology can be used to print the Dekton® slabs with the design which the client or professional wishes to use, so achieving amazing results.  The material’s excellent technical performance is maintained over the entire surface, including the areas where the customisation has been applied.