Press Release,

Cantoria, January 2015

“House of Dekton®”

Technical Information

- The House of Dekton®, designed by Steffen Kehrle is made entirely of Dekton® ultra compact surfaces and a steel frame.

- A new system without any visible connections has been developed for hooking the panels to the frame.

The iconic House of Dekton® is not only impressive in terms of architecture and design, but also features a perfectly balanced structural support frame. The 14-sided house is made entirely from the ultra-compact Dekton® surface; more than 120 custom-made slabs of different sizes with a total surface area of 250m2 are used to create the interior and exterior walls, the floor and ceiling, as well as a continuous circular bench and a table. The slabs are mounted to a steel frame without any visible joints or connections: the pavilion’s load-bearing structure is created using crossbeams made from both chamfered profiles and steel girders used as gallows. In collaboration with a structural engineering office and a metalworking firm, designer Steffen Kehrle has developed a solution by which the Dekton® slabs can be hooked to the steel frame without any visible joints or connections: blind holes were drilled into the 1.2cm thick slabs and, using a special adhesive, sleeves were glued to the holes. The sleeves can be easily hooked into the steel frame. The system also allows disassembling and re-erecting the house.

The Dekton® slabs are cut with waterjets and circular saws fitted with specially developed discs for cutting Dekton®. Icons, which represent the various properties of Dekton®, were engraved in the wall and floor panels. Special engravings were also applied to the exterior wall slabs at the left and right hand side of the entrance. Steffen Kehrle designed a pattern based on the House of Dekton® floorplan. The pattern is also reminiscent of ornamental Andalusian tile patterns and refers back to the home of Dekton®: the Cosentino group’s headquarters are located in Cantoria, near Almeria, in the south of Spain. The engravings are just one example of the many ways in which architects or designers can customise Dekton slabs. Developed by Cosentino’s in-house R&D department, innovative ‘Technology of Sinterized Particles (TSP)’ allows the production of large-format slabs (3.20m x 1.44m) in any desired colour or finish.

The light dome is quite literally one of the House of Dekton’s highlights. The 14 ceiling slabs are mounted at an angle so as to leave a central opening with a diameter of 1.5m. The opening is fitted with fluorescent tubes to create a ‘sky’ of light that illuminates the house in such a clever way that almost no shadows are created. The dimmable lights can create different moods; for example, the house’s sculptural character comes to the fore particularly well at low light intensity.

The House of Dekton® design is 4.55m high, with a diameter of 6.50m and a total weight of 10,075kg. (The adapted version at BAU has a total weight of 8,350kg.)

“House of Dekton®“ Project Partners:

Structural engineering: Ingenieurbüro Karl Wagner, Herrsching/Ammersee

Metalworking: Ludwig Michl GmbH, Waakirchen

Stone Processing: Marmor-Center GmbH, Römhild

Design and Project Management: Steffen Kehrle, Munich

BAU - Munich: 19-24 January - Halle A 4, Booth 301

Stockholm Furniture Fair - Stockholm: 3 - 7 February – Booth A42:16

Made Expo - Milan: 18-21 March

Construmat – Barcelona: 18-22 May

Media Contact:

Chloe MacDonagh or Francesca Sanchez

Sellers PR

01962 977950

Francesca@sellerspr.com | Chloe@sellerspr.com

Follow us: @CosentinoUK

Like us: www.facebook.com/cosentinouk.ie

Find out more: http://uk-ie.cosentinonews.com/

About Dekton® by Cosentino

The ultra-compact surface, Dekton® by Cosentino is a new and innovative category of surfaces created with the objective of becoming a global leader in the world of architecture and design both for indoor and outdoor spaces.  It is the result of an investment of 128 million euros and 22,000 hours of research and development, making it the perfect partner for designers and architects throughout the world.

Dekton® is a sophisticated mixture of the raw materials that is used to manufacture glass, porcelain materials and quartz surfaces. The Dekton® surface can recreate any type of material with a high level of quality. It is manufactured in large format (320 cm x 144 cm) and thin thicknesses (0.8 cm, 1.2 cm and 2 cm) and it has superior technical characteristics:

      - High mechanical resistance

      - Good resistance to fire and heat

      - High scratch resistance

      - High UV rays resistance

      - High hydrolysis resistance

      - Low porosity

      - Very good colour stability

      - Very good dimensional stability

      - High abrasion resistance

      - High stain resistance

      - Resistance to freezing and thawing.

These superior technical characteristics are achieved thanks to the exclusive TSP (Technology of Sinterized Particles), developed by the R&D of Cosentino Group. TSP technology is an ultra-compaction process which makes Dekton® a totally revolutionary low-maintenance, long-lasting product with a multitude of applications.

Prestigious architect and designer Daniel Libeskind created in 2014 “Beyond The Wall”, a spectacular sculpture which becomes the first architectural and design milestone created with Dekton® by Cosentino. As well, the ultracompact surface Dekton was selected for the flooring of Baku airport, Pepe Jeans stores in Barcelona, Paris and Rotterdam, Dani García restaurant in Marbella (two Michelin stars) and DiverXO restaurant from David Muñoz (three Michelin stars) in Madrid.

Since 2011, the Cosentino Group is a sponsor and official provider of worktops at “The 50 Best Restaurants of the World”. Since 2014 with its Dekton® brand sponsoring the “One To Watch” award.

In 2015, the Spanish tennis player Rafa Nadal features in a worldwide Dekton® adversiting campaign. At the same time, thanks to Cosentino’s sponsorship of the project “Rafa Nadal Academy by Movistar” the tennis academy will include Dekton in diverse applications of the spectacular premises.

www.dekton.com

About Cosentino Group

The Cosentino Group is a global, family-owned company that produces and distributes high value innovative surfaces for architecture and design. As a leading company, Cosentino imagines and anticipates together with its customers and partners design solutions that offer value and inspiration to people’ lives. This goal is made possible by pioneering brands that are leaders in their respective segments such as Silestone®, Dekton® and Sensa by Cosentino®. Technologically advanced surfaces which allow the creation of unique designs for the home and public spaces.

The group bases its development on international expansion, an innovative research and development program, respect for the environment and sustainability, and its ongoing corporate commitment to society and the local communities where it operates, education, equality and health & safety.

The Cosentino Group currently distributes its products and brands in more than 80 countries, and directly manages from its headquarters in Almeria (Spain) its own facilities in 29 of them. More than 90% of the Cosentino Group’s turnover comes from international markets.

www.cosentino.com |www.silestone.com| www.dekton.com| www.sensabycosentino.com